## Slide 1: Museum Exposure Limiter
VARIANT 10.03 | ESD AND IOT + MACHINE LEARNING
LumiTrack: keep cumulative light below a target while retaining visibility
NUCLEO-F446RE + servo + LDR

## Slide 2: Problem and real-time use case
01 | WHY
1
The problem
An LDR sees light only where it points. Museum light is diffuse, directional, obstructed or changing, so one reading cannot protect an artifact.
2
Real-time use
A smart showcase scans the light field, estimates exposure risk and tilts a shade to a safe angle, then keeps re-checking as visitors, windows and lamps change.
3
Objective
Keep cumulative light under a target while the exhibit stays visible. Fewer scans, fewer unsafe angles, no manual tuning.
Live loop: scan, classify, command, acknowledge, re-scan on drift.
LumiTrack | Variant 10.03 | Museum Exposure Limiter | NUCLEO-F446RE | 2 / 12

## Slide 3: System architecture
02 | ARCHITECTURE
Sense
LDR divider into the 12-bit ADC, ambient reference, temperature channel, target-band potentiometer.
→
Actuate
Servo on timer PWM, external fused 4.8-6 V supply, travel stops.
→
Link
USART2 over the ST-LINK virtual COM port. OLED or LEDs show state.
→
Decide
Host Python runs features and models. The F446RE validates every command.
Firmware: ESD CO-1 to CO-3 | Models and evaluation: ML M2, M3, M5, M6
LumiTrack | Variant 10.03 | Museum Exposure Limiter | NUCLEO-F446RE | 3 / 12

## Slide 4: NUCLEO-F446RE and wiring plan
03 | HARDWARE
Block | Parts | Rule
Controller | NUCLEO-F446RE (Cortex-M4F, 180 MHz), laptop | Build, flash, debug
Sensing | LDR + fixed resistor on PA1 (ADC1_IN1) | 0-3.3 V, RC filter
Actuator | Servo signal on PA0 (TIM2_CH1) | Never powered from GPIO
Fixture | Museum case emulator, artifact-plane LDR, shade | Repeatable positions
Protection | Fused 5 V supply, power switch, common ground | Separate fused branches
Board note: the course syllabus uses the H743, but F4 concepts are the same. CAN here is bxCAN, not FDCAN.
LumiTrack | Variant 10.03 | Museum Exposure Limiter | NUCLEO-F446RE | 4 / 12
Notes: Pins are suggestions; confirm against the Nucleo-64 pinout before wiring.

## Slide 5: Firmware design (STM32F446RE)
04 | EMBEDDED
1
Peripherals
TIM2 PWM about 50 Hz for the servo. ADC1 with DMA and oversampling for the LDR. USART2 for the host link. GPIO for LEDs.
2
Control flow
A basic timer interrupt (TIM6) drives the scan tick, not polling. Settle delay, then average N samples. Out-of-range angles rejected.
3
Protection
IWDG watchdog, host timeout, fault latch, safe-home state. Angle and slew limits live in the MCU.
States: IDLE, SCAN, HOLD, MOVE, RETURN_HOME, FAULT
LumiTrack | Variant 10.03 | Museum Exposure Limiter | NUCLEO-F446RE | 5 / 12

## Slide 6: Host and MCU protocol
05 | PROTOCOL
Command | Meaning | MCU response
ANGLE_ID | Move to an approved angle | ACK or REJECT + reason
SCAN_PROFILE | Run partial or full scan | Profile stream + ACK
HOLD | Stay at current angle | ACK
RETURN_HOME | Go to safe neutral angle | ACK, always allowed
Every message carries model version, confidence band, sequence number and expiry. Stale or unknown commands are refused.
LumiTrack | Variant 10.03 | Museum Exposure Limiter | NUCLEO-F446RE | 6 / 12

## Slide 7: Data collection plan
06 | DATA
1
What we record
Servo angle, LDR voltage, ambient level, scan direction, sample time, position quality, temperature.
2
Metadata
variant_id, condition_id, run_id, target level, calibration version. A scan is one independent example.
3
How much
6-10 short safe runs per state plus organiser seed data. Split by run or session, never adjacent scans.
Output: labelled dataset, data dictionary and quality checks.
LumiTrack | Variant 10.03 | Museum Exposure Limiter | NUCLEO-F446RE | 7 / 12

## Slide 8: Machine learning approach
07 | MACHINE LEARNING
Step | Detail
Features | Peak intensity, peak angle, curve asymmetry, angle gradient, total exposure, temperature
Task A | Classify exposure risk: safe, caution, dangerous
Task B | Regress best safe angle
Models | Ridge logistic regression, then gradient-boosted tree
Baseline | Fixed-angle exhaustive scan, maximum LDR value
Classification or regression is the default; clustering only where already covered.
LumiTrack | Variant 10.03 | Museum Exposure Limiter | NUCLEO-F446RE | 8 / 12

## Slide 9: Evaluation and nearest confuser
08 | EVALUATION
1
Metrics
Confusion matrix, macro-F1, recall of the dangerous class, angle error, intensity regret, scan-time saved.
2
Validation
Stratified CV grouped by run, held-out physical runs, confidence calibration, learning curve.
3
Hard cases
Two nearest states, noisy local peak, reflection, partial shadow. Prove it beats a simple threshold.
Report error by load, direction, temperature and lighting regime.
LumiTrack | Variant 10.03 | Museum Exposure Limiter | NUCLEO-F446RE | 9 / 12

## Slide 10: Safety, faults and live acceptance
09 | SAFETY
1
Safe behaviour
Bounded speed and travel. Host timeout or manual override returns to neutral. The MCU decides whether a prediction is applied.
2
Faults handled
Host lost, ADC out of range, stale command, servo limit, watchdog reset. Faults are latched and reported.
3
Live test
Reference run, target run, nearest-confuser run with telemetry, ACK and physical outcome. Then unplug the host and show safe state.
LumiTrack | Variant 10.03 | Museum Exposure Limiter | NUCLEO-F446RE | 10 / 12

## Slide 11: Team roles (4 members)
10 | TEAM
1
[K.Sai babu] Firmware
Timers, PWM, ADC DMA, USART2, watchdog, state machine.
2
[M.L.N.Manikanta] Hardware and safety
Fixture, wiring, fused supply, travel stops, calibration.
3
[Ch.Bhuvan]
Data and ML
Dataset, features, baseline, ridge and tree models, plots.
4
[K.Eswar] Integration
Host service, protocol, README, demo video, live test.
Everyone joins the reviews and the live acceptance.
LumiTrack | Variant 10.03 | Museum Exposure Limiter | NUCLEO-F446RE | 11 / 12

## Slide 12: Timeline, reviews and deliverables
11 | DELIVERY
Review | Evidence
R1 Design | Geometry, scan angles, light regimes, safe neutral
R2 Embedded | Repeatable scan, tagged angles, bounded commands
R3 Data | Dataset, quality checks, brightest-sample baseline
R4 ML | Angle error, regime model, unseen locations
R5 Integration | Partial-scan positioning, host-loss test, override
Final | Blind light configuration vs baseline scan policy
Deliver: firmware, protocol, dataset, notebook, test report, demo video, README.
LumiTrack | Variant 10.03 | Museum Exposure Limiter | NUCLEO-F446RE | 12 / 12